## Slide 1
Wellbore Expandable Tubular - Progress, Issues and Challenges
Prof. Tasneem Pervez
Assistant Dean for Postgraduate Studies and Research
Project Leader, Applied Mechanics and Advanced Materials Research Group
Sultan Qaboos University, Oman

## Slide 2: Materials & Design
Natural-desire or Demand-driven Improvements
New/update Design
or Processes
Emerging Materials
or Improvements
in Existing Materials
Subsequent Developments
Expose Limitations
New Opportunities
New Challenges
Materials
& Design
Stone – Metals –
Polymers – Composites –
Tailored materials

## Slide 3: Tailored Materials
Macro-to-Micro
Scale

## Slide 4: Why Tailored Materials?
The engineers and scientists develop tailored materials:
To have better safety
To do things which were not doable before
To have improved properties
To fulfill demands of design/tools/processes
To save/preserve/store energy
To have better health/environment
To have better affordability

## Slide 5: Better Safety !!!

## Slide 6: To Do Things not Doable Before
Oil and Gas Wells Design, Drilling and Delivery
Reach Deep and Scattered Reservoirs
5 km +++ to 9 km +
Tap from Difficult to Access Reservoirs
Improve Well Production Life
Better Material Unavailability
Reduce Cost (Number of days required to drill a well, Size of the rig, Tools …….)
10 M USD to 360 M USD

## Slide 7
Eliminate floater &
Subsea tie-in - MoD
X

## Slide 8: Slim-to-MoD Wells
36"
26"
20"
16"
9-5/8"
7"
11-3/4"
13-3/8"
Telescopic Well
5-1/2”
TD = 5 Km +++
The Vision
Mono-diameter Well
S
L
I
M
Well
Benzie et al, 2002

## Slide 9: Game Changer
Solid Expandable Tubular Technology

## Slide 10
Strength of Expandable Liner Hangers;
Mechanics of SET in Irregularly Shaped Boreholes;
Mandrel pop-out and its effect on well integrity;
Solid Tubular Expansion in Horizontal Wells;
Dynamic Effects on SET
Formation Flow Around Annular Barriers such as
Open Hole Clads or Scab Liners;
Design, construction, audit and commissioning of a
Expandable Tubular Test Rig (ETR)
Crystal Plasticity based FEM
Macro-scale Experiments
Microscopic Investigations
Understanding Macromechanics in terms of
Micromechanics (M3 Microstructure)
Nature and Scale of Problems

## Slide 11
Expandable Tubular Test-Rig

## Slide 12
Expandable Tubular Test-Rig

## Slide 13
Creating a launcher
400 Tons hydraulic press
Expandable Tubular Test-Rig

## Slide 14
Mechanical Expansion Test of SET in SQU on May 21st 2008.
(7 5/8”, 15% ER,
OD actual 8.7” v/s Enventure’s 8.662”)
Expandable Tubular Test-Rig

## Slide 15
Real Time Data Acquisition
Expandable Tubular Test-Rig

## Slide 16
16
Experimental
FEA
Some Results ........

## Slide 17: Pop-out Problem Formulation
The tubular, inner and outer fluid layers are uniform and homogenous.
The formation is impermeable.
Steady state fluid velocity is low.
Tubular material is elastic-perfectly plastic.

## Slide 18: Mathematical Model
Using continuity of mass and momentum of fluids, and the equation of motion, the wave equations associated to the inner fluid, elastic-perfectly plastic tubular and the outer fluid can be expressed as follows:

## Slide 19
7.625” OD SET, 14.1% expansion, 7.902” Drift
Some Results ........

## Slide 20: Dynamics of Stick-Slip
  Check stick criterion
Governing Equations:
  Velocity state equation
  Acceleration state equation
  Stick-time state equation
  Slip-time state equation

## Slide 21
  Contact pressure:
  Expansion force:
  Thickness variation:
  Length variation:
  Static friction force:
  Kinetic friction force:

## Slide 22
ID=7.200”, OD=8.000”, t = 0.400”, ER= 20%
Some Results ........

## Slide 23
Current Challenges
  Preserving structural integrity; current expansion leads to 50% reduction in collapse pressure rating making it unsuitable for well applications.
  Increased expansion ratio; desires to reach 30% and above; currently possible 28% in laboratory setup and 18.64% in field applications.
  Existing rig capacity; needs to reduce force required for expansion; current rigs with capacity of 250 tons are not suitable.
Search for New / Tailored Materials
  High strength and formability
  Reliability and Long Life
  Lower expansion force and reduced cost
Issues and Challenges

## Slide 24
Current Area
of Research
LSX80
Sour X70
DP
VM50
X52
DD13
5
10
15
20
25
30
35
40
100
200
300
400
500
600
700
800
0
0
Strain, %
Stress, MPa
Low strength, high ductility
Intermediate strength, Low ductility
Intermediate strength, hardening ????
AHSS
Current Tubular/ Casing Steel
Current Research on X-Steel

## Slide 25
Tailored AHSS can provide extremely high-strength, while maintaining the minimum limit of formability required for large expansions
AHSS were developed based on selected chemical compositions and multiphase microstructures through precisely controlled heating and cooling processes
New/Tailored Materials
Phases of interests are Austenite, Martensite, Ferrite/Bainite, and retained austenite after transformation of phases due to TRIP and/or TWINNING

## Slide 26
26
Martensite
Harder & tougher phase
Forms in plates/laths
Makes it like composite
Preferred orientation of laths
Tailored material properties
New/Tailored Materials

## Slide 27
Understand macromechanics in terms of micromechanics
M3 Microstructure

## Slide 28
Research Methodology

## Slide 29
EBSD on polycrystalline
1
1
2
3
4
5
6
Microscopic Investigations

## Slide 31
Crystal Plasticity FEM

## Slide 32
Analytical, macro/micromechanical models are developed and finite element simulations are done to predict the elastic-plastic behavior of single and polycrystalline materials
Models are in good agreement with the available experimental and simulation results
CPFEM model can be used to simulate behavior of many crystalline materials at macro-level taking into consideration its micro-level characteristics including: crystal type, texture information, etc.
State-of-the-art experimental testing facility that can be used to study materials at submicron-level under various thermo-mechanical loading conditions will help in establishing a better understanding of the material behavior at macro-level making the tailored material approach more visible
Conclusions

## Slide 33
Acknowledgements
Many thanks and appreciation to TRC/PDO for funds.
Special thanks go to doctoral and Master students’ for their dedication, hard-work and perseverance to obtain excellent research outcomes
Special thanks to Said Al-Houqani, Bader Al-Abri, Mark van de Velden, Victor Ogoke, Dr. Paul Francis, Dr. Franz Marketz, Sulaiman Al-Mandhari, Abdulsattar Al-Murshidi, Shaikhan Al-Khoudori for their direct and indirect valuable comments and discussions.
We cannot forget the valuable discussions with Shell research team as and when we needed their assistance, particularly Mr. Ton Wubben.
Last but not the least is the support of our families, who are still bearing with us for long after-office work hours.
“To all the team members of AM2RG”

## Slide 34: Thank you for your attention

## Slide 35
Thank you very much for your presence

## Slide 36
Oil & gas industry needs those metals which have high strength and good formability properties
Deform Easily and
Retain Strength & Integrity
Working envelope
Stress
Strain
UTS
YS
Stress
Strain
1
2
3
4
a
b
c
d
New/Tailored Materials

## Slide 37
Macro Level
Meso Level
Micro Level
Crystal Level
Kinetics & Kinematics
Micromechanics
Grain Mechanics
Tubular Material Behavior
M A
Adopted Approach