## Slide 1: 5th International Mechanical Engineering Congress
THEORETICAL ENERGY AND EXERGY ANALYSIS OF A SOLAR THERMAL DESALINATION SYSTEM USING PASSIVE VACUUM
Engr. M. Ihsan Ul Haq National University of Sciences & Technology, Islamabad
9th and 10th May, 2015

## Slide 2: Presentation Scheme
Introduction
Desalination
  Brief History of Desalination
  Solar Desalination
Process Configuration
Energy Analysis
Exergy Analysis
Results and Discussion
Conclusion

## Slide 3: Introduction
Why Desalination ?
World Health Organization Facts:
  About 3.4 million deaths occur in each year due to water related diseases.
  Nearly one out of each 5 deaths of children under the age of 5 years in the world is due to water related diseases
  About 1.8 billion of population will be living in regions of complete water shortage by 2025.
  For every one dollar invested in water and sanitation, there is an economic return of three to four dollars

## Slide 4: Introduction
Why Desalination ?
United Nations Organization Facts:
  Top priority to problem of water scarcity
  Nearly 450 million people in 29 countries are living in water deficient regions
  More than 1 billion people are not getting safe drinking water
  Nearly half of the world’s population is lacking water purification plants.
  In the third world countries, nearly 50 % of diseases are due to use of contaminated water.

## Slide 5: Desalination
A process of producing potable water by removing dissolved salts from saline or brackish water
Conventional desalination processes affect:
  Energy
  Economy
  Environment
To produce 1000 cubic meter per day of potable water need 10,000 tons of oil per year.
Industrial Applications

## Slide 6: Brief History of Desalination
Aristotle : Water cycle is a huge solar energy open distillation plant
Alexander : Desalination of seawater was being carried out by sailors
Wheeler and Evans: First patent on solar desalination in 1870
Carlos Wilson: First solar desalination plant in 1872.
Al-Kharabsheh and Goswami: Solar desalination by passive vacuum technique in 2009.

## Slide 7: Solar Desalination
Direct Solar Desalination:
Solar energy is used directly to produce potable water.
For example, Solar Stills
Indirect Solar Desalination:
Saline water is heated separately in solar collector
Hot water is fed in flashchamber
For example, Solar Multi Stage Flash Desalination unit

## Slide 8: Concept of Passive Vacuum
This concept can be understood by following equation:
    where;
        P = 101325 Pa
        ρ = 997.04 kg/m3
        g = 9.81 m/s2
    Hence,
        h = 10.37 meters
  Therefore, theoretically vacuum will be generated passively if the chamber is placed at 10.37 meters height from the ground with hydrostatic balance.

## Slide 9: Effect of Pressure on Evaporation
The decrease in the pressure of evaporation chamber causes increment in the rate of evaporation of feed water.
Chart: Pressure vs Evaporation rate
| 10 | 13.89 | 17.78 | 21.67 | 25.56 | 29.44 | 33.33 | 37.22 | 41.11 | 45
Evaporation rate vs gauge pressure in vacuum chamber | 59.89 | 48.71 | 39.85 | 32.44 | 26.03 | 20.73 | 15.27 | 10.62 | 6.337 | 2.363

## Slide 10: Calculation of Area of Solar Collector
To increase temperature of 1 kg of water to 1 0C, we need energy of approx. 4200 Joules.
Total energy required for heating:
Energy utilized by collector:
Area of solar collector:
Where;
─ Mass flow rate of water
e ─ Energy required to
increase temperature
─ Average solar irradiance
─ Area of solar collector

## Slide 11: Generation of Passive Vacuum
Water is pumped in the evaporation chamber and condenser with open valve on top only.
After complete filling, Valve on top is closed.
Valves of Fresh water tank and brine water tank are opened.
Water flows down under the action of gravity and vacuum is generated in condenser and evaporation chamber.

## Slide 12: Process Configuration
The saline water is first preheated in the condenser.
The preheated saline water then enters in the solar heater
Hot Water flashes in the evaporator after passing through the expansion orifice.
The fresh water and concentrated brine flow down to the ground tanks due to gravity.
Vacuum is maintained by the hydrostatic balance between the elevated vessels and the ground

## Slide 13: Process Configuration
Video

## Slide 14: Process Configuration
Different state points of system:

## Slide 15: Energy Analysis
Energy:
Energy is capacity of a physical system to do work
Energy can be transferred through:
  Heat
  Work
Assumptions:
Overall heat transfer coefficient is constant.
Heat losses are negligible.
Phase change occurs in the condenser.
The shell temperature is constant at any cross section.
Ambient temperature is 25
Density of saline water and potable water is 1000 kg/

## Slide 16: Energy Analysis
Mathematical Models:
Evaporation chamber:
Condenser:
Solar Collector:
Pump:

## Slide 17: Exergy Analysis
Exergy:
Exergy is a measure of maximum useful work that can be done by a system interacting with an environment .
Exergy loss is determined by the product of absolute temperature of surrounding and entropy increase.
Assumptions:
Overall heat transfer coefficient is constant.
Heat losses are negligible.
Phase change occurs in the condenser.
The shell temperature is constant at any cross section.
Reference ambient temperature is 25
Density of saline water and potable water is 1000 kg/

## Slide 18: Exergy Analysis
Mathematical Models:
Evaporation chamber:
Condenser:

## Slide 19: Exergy Analysis
Mathematical Models:
Solar Collector:
Pump:

## Slide 20: Results and Discussion
Input Parameters:
Temperature and pressure values at different state points
Salt concentrations
Potable water flow rate
Solar irradiance
Density of water
Ambient temperature
Efficiency of pump

## Slide 21: Results and Discussion
Output Parameters:
Quality of vapours
Evaporation rate
Heat supplied
Energy required for pump
Energy and exergy efficiencies
Saline water and brine flow rates.
Exergy destruction in condenser, evaporation chamber, pump and solar collector

## Slide 22: Results and Discussion
Energy Efficiency
11.74 %
Exergy Efficiency
5.12 %

## Slide 23: Results and Discussion
Output of EES Software:
Quality of vapours is 3.547 % at pressure of 20 kPa.
Power needed for desalination is approx. 2.6 kW of potable water.
For 50 Litres output:
Power needed for desalination is 14.39 kW.
Power supplied in solar collector is 13.28 kW.
Power recovered in condenser is 1.106 kW.
Area of Solar Collector is 34.4 m2

## Slide 24: Results and Discussion
Pressure Vs Quality
Reduction in the pressure of the evaporation chamber, at a certain temperature, increases the quality of vapours formed.
Chart: Pressure of evaporation chamber (kPa)
| 10 | 13.89 | 17.779999999999987 | 21.67 | 25.56 | 29.439999999999987 | 33.33 | 37.220000000000013 | 41.11 | 45
Chamber Pressure vs Quality | 0.05989 | 0.04871 | 0.03985 | 0.03244 | 0.02603 | 0.02037 | 0.01527 | 0.01062 | 0.006337 | 0.002363

## Slide 25: Results and Discussion
Solar Collector Temperature Vs Quality
Increase in the temperature of water in solar collector, at a certain pressure (20 kPa), increases the quality of vapours.
Chart: Solar Collector Temperature (◦C)
| 70 | 71.11 | 72.22 | 73.33 | 74.440000000000026 | 75.56 | 76.669999999999987 | 77.78 | 78.89 | 80
collector temperature vs quality | 0.0177 | 0.01967 | 0.02164 | 0.02362 | 0.02559 | 0.02757 | 0.02954 | 0.03152 | 0.03349 | 0.03547

## Slide 26: Results and Discussion
Pressure Vs Energy For Desalination
Reduction in the pressure of the evaporation chamber, at a certain temperature, reduces the energy needed for thermal desalination
Chart: Pressure of Evaporation Chamber (kPa)
| 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
 | 2504 | 2513 | 2520 | 2526 | 2531 | 2536 | 2540 | 2544 | 2548 | 2551 | 2555 | 2558 | 2560 | 2563 | 2566 | 2568 | 2570

## Slide 27: Conclusion
Solar flash desalination system is a promising approach to tackle:
    Water Crisis
    Energy Crisis
    Environmental Pollution
Water can be desalinated at low temperature by generation of passive vacuum on the surface of water and thus require less thermal energy

## Slide 28: Conclusion
The promising approach is the use of solar energy, latent heat of condensation and passive vacuum technique to increase the energy efficiency of the desalination system
Applications:
    Islands
    Coastal Areas
    Water Scarce Remote Areas

## Slide 29: Acknowledgement
Dr. Shafiq-ur-Rehman Qureshi,
  Dean of Engineering Sciences Department,
  NUST-PNEC
    Supervision
    Support
My Parents
    Encouragement
    Support

## Slide 30: References
[1] | P. Shinde, “Water Scenario 2025,” Water Management Scenerio 2025 Problems, Issues and Challenges, 2005.
[2] | S. Kalogirou, “Seawater desalination using renewable energy sources,” Progress in Energy and Combustion Science, pp. 242-281, 2005.
[3] | M.Salem, “Solar Desalination as an Adaptation Tool for Climate Change Impacts on the Water,” 2013.
[4] | R. S. Silver, “Silver Engineering”. London Patent 829,819, 25 September 1957.
[5] | J. H. Beamer, D. J.Wilde, “The simulation and optimization of a Single Effect MSF desalination plant,” Desalination, pp. 259-262, 1971.
[6] | E. Howe, Fundamental of Water Desalination, New York: Marcel Dekker, 1974.
[7] | S. Khan, “Desalination Technology: An intensive course,” Porthan Ltd, 1992.

## Slide 31: References
[8] | S. Al Kharabsheh, D.Y. Goswami, “Analysis of an innovative water desalination system using low-grade solar heat,” Desalination, vol. 156, pp. 323-332, 2003.
[9] | M.Abutayeh, “Theoretical and Experimental Simulation of Passive Vacuum Solar Flash Desalination,” University of South Florida, 2010.
[10] | S.C.Maroo, Theoretical Analysis of Driven Flash Desalination System Based on Passive vacuum Generation, 2006.
[11] | V.G. Gude, N. Nirmalakhandan, S. Deng, A. Maganti, “Desalination at low temperatures: an exergy analysis,” Desalination and Water Treatment, vol. 40, pp. 272-281, 2012.
[12] | H.M.Qiblawey, Fawzi Banat, “Solar thermal desalination technologies,” Desalination, pp. 633-644, 2008.
[13] | V. G. Gude, “Energy storage for desalination processes powered by renewable energy and waste heat sources,” Applied Energy, 2014.
[14] | J. Lablanc, “Solar Thermal Desalination-A modelling and Experimental Study,” Australia, 2009.

## Slide 32: Questions & Answers

## Slide 33: Thank You